## Slide 1: CSBridge – Net 5
Prof. Katz

## Slide 2: User Datagram Protocol (UDP)
A simple, connection-less layer 4 protocol for the transmission of non-critical data
No reliability, No confirmation of delivery, No order of packets!
Very Light protocol which sits on top of IP layer.
Used by a number of ULPs including DNS, DHCP, and BootP.

## Slide 3: Port numbers
UDP introduces the concept of port numbers as a layer 4 address.
Ports are used to indicate which layer 7 service should receive the packet and which produced it.
When a server program starts it “binds” to the port it will use for communication (usually <1024), UDP then knows that data received for that port should be delivered to that program.

## Slide 4: Ports (cont.)
When a client service begins communication it can either request a specific port for communication or use a unique port provided by the OS.
Server ports are static, client ports may be dynamic.

## Slide 5: Common UDP port numbers
67 – BooTP Server
68 – BootP client
69 – Trivial FTP

## Slide 6: UDP Header

## Slide 7: Header Values
Source port – The port on the source host which generated this message
Destination Port – The port on the destination host which should receive this message
Length – The length of the header and data

## Slide 8: UDP Checksum
The UDP checksum is calculated across the data and the header.
The Checksum is the one’s compliment of the 16-bit sum of the words in the header and data.
Additionally the 32-bit source and destination, the 8 bit protocol field, and the UDP length are included in the sum.

## Slide 9: UDP Generated Header

## Slide 10: UDP Checksum
On the receiving end all words are added to the checksum and the result should be all ones.
If the result is not all ones then an error has occurred.

## Slide 11: UDP in action (DNS demo)

## Slide 12: Transport Control Protocol
Provides a connection oriented layer 4 service
Provides guarantees
Provides sequence ability

## Slide 13: TCP Header
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 1 0 | 1 1 | 1 2 | 1 3 | 1 4 | 1 5 | 1 6 | 1 7 | 1 8 | 1 9 | 2 0 | 2 1 | 2 2 | 2 3 | 2 4 | 2 5 | 2 6 | 2 7 | 2 8 | 2 9 | 3 0 | 3 1
Source Port |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Destination Port |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sequence Number |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Acknowledgement Number |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Header len |  |  |  | reserved |  |  |  |  |  | URG | ACK | PSH | RST | SYN | FI N | Window size |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Checksum |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Urgent Pointer |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Options + padding |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 14: TCP Header (cont.)
Source and destination ports – Which application produced the packet and which should receive it
Sequence number – Identification of the relative location of the first byte in the packet to the first byte in the stream.
Acknowledgement number – The sequence number of the next byte which the receiving station expects

## Slide 15: TCP Header (cont.)
Urgent
Acknowledgement
Push
Reset
Synchronize sequence numbers
Final packet

## Slide 16: TCP Connection Establishment
Client Sends SYN
Server Replies with SYN-ACK
Client Replies with ACK

## Slide 17: TCP Connection maintenance
The Sequence number is incremented for every packet sent
An acknowledgement must be made before the window size is reached.
An ack is sent for the next byte which the client expects to receive.

## Slide 18: TCP State Diagram